Met Rear 3-piece Window

Installing EARLY Met 1954 Rear 3-piece glass

8/16/05

We do it all the time here, but the one-piece rear window is the most challenging to install.  I'll take you through the steps (this operation takes 3 a minimum of 3 people)

- Install stainless trim in upper rubber.

- Fit upper rubber/trim to car and hold in place with masking tape.

- Lay lower rubber in place.

- Soap upper & lower glass grooves in rubber (do not use silicone).

- Offer glass up to top rubber first, working a little back & forth at first, use a glass hook to assist.

- After getting the glass started in the upper rubber, start working the lower rubber using glass hooks.

- Hold steady pressure along the bottom of the glass and work alternately between the lower and upper rubber.  After a little work, the glass will be in place, but the lower part will not be completely in place.

- From the inside, using the holes in the lower pinch weld, drill through the lower rubber (make sure you aim low enough & stay clear of the glass).

- Soap the newly drilled holes from the outside.

- Install new retaining bolts into the belt moulding trim and offer it up to the lower rubber, lining up the new bolts to your newly drilled & soaped holes.

- Push the belt moulding into place and install nuts on the retaining bolts (this takes some time and effort).

- Slowly and evenly tighten the nuts on the retaining bolts.  As you tighten the nuts, the lower glass and belt moulding will gradually pull into place.

- After the glass is fully seated, cut of the retaining bolts excess length.

- Install the 'Y' trim pieces at the corners of the glass.

As you can see from this sequence, the glass is not fully pulled into place until the belt moulding is installed.  Experienced workers can perform this process in approximately three hours.  If they haven't done this before, it will probably take most of the day.  Don't serve beer until you're finished.

Kip Motors