LATER Metropolitan INTERCHANGE PARTS

4/22/05  (xxx-xxx = Moss Motors number)   (prices approximate)

Later BRAKES

Adjuster Assembly							582-280 or LUCAS 64271022	 or 37H6134)		$29x2

FRONT wheel cylinder 						QH   BWC-3260										$25x2

FRONT wheel cylinder 						QH   BWC-3261										$25x2

REAR wheel cylinder 						DELPHI   LW-33476								$27x2

REAR Fitting wheel kit with clips

& Dust Covers								582-225	 or (GRSP 2862)							$18

REAR retaining PINS						Raybestos   H1080							 		45¢x4

BRAKE HOSES

Front hose									Raybestos   BH 35046								$20x2

Rear											Raybestos   BH 36903								$27x1

HEATER VALVE

RANCO Rubber SEAL 						NAPA 660-1000										$12

Heater Duct Hose (Black)					456-170 (11")										$7

Heater Duct Hose	(Black)				456-185 (19")										$13

1500cc ENGINE PARTS (Moss Motors)

Rod BEARING (Standard)					425-700												$29

Frost PLUGS									328-230												80¢x4

CLUTCH

Pressure Plate								190-120												$105

Clutch Disc									190-140												$65

Throw-out Bearing							190-290												$22

Ring Gear									190-040												$45

5/8" Master cylinder							LUCAS   311 2247									$109

Clutch Slave Cyl HOSE (2" longer)		DELPHI  180 355 or LH 5164 or GBH 110		$18

ELECTRICAL

Front Turn Signal Rubber Sockets		158-300												$15x2

Front Headlamp    							12-Volt BULB GE 6012 - 6014 - H6024 - 6024

Front Turn Signal       						12-Volt BULB Double filament						1016

Rear-Brake                						12-Volt BULB Double filament						1016

Rear-Turn Signal        						12-Volt BULB Single filament						1141

Rear License Plate     						12-Volt BULB single filament						57

THESE Tune-Up NUMBERS WERE GOOD 8/9/04

Points        									Blue Streak    										LU-1617XP

Condenser 									Blue Streak    										LU-206

Rotor         									Blue Streak    										LU-300

Distributor CAP 								Blue Streak    										LU-420

Spark Plugs          							NGK BPR 5ES 										(7734)

Spark Plugs 									Champion 											RN 5C

Plug Wires   									Blue Streak EC 9409 								(354001)

Both of these are resistor plugs and are supposed to be gapped at .025.

Cartridge Oil FILTER  WIX  			 	51-300 				CarQuest # 85300)

Fan Belt										Beck/Arnley	141-1200 	9.5x888 smooth

Heater Valve Seal 							NAPA/Balkamp/RANCO BK 660-1000 water valve

ALUMINUM Inside wire-tube

Defroster DUCT 								NAPA 												819-1127

Rear Brake HOSE							Raybestos											BH 36903

Front Brake HOSE							Raybestos											BH 35046

REAR Axle Parts from Moss Motors for a Sprite-Midget

125-830		$16.95		HUB BEARING KIT

(gasket, oil seal, O-ring, bearing, tab washer)

# 3				265-560		$2.00			TAB WASHER

#35			296-030		$0.95			Hub Paper GASKET

#36			120-030		$4.95			Oil SEAL

#37			121-410		$1.95			O-RING

#38			125-120		$12.95		Hub BEARING

#7				294-210		$1.60			Differential Paper GASKET

#28			120-800		$2.95			Pinion OIL SEAL

#38			180-200		$9.95			Clutch Slave Cylinder PUSH ROD 2½”

#39			582-590		$0.90			Clutch Slave Cylinder CLEVIS PIN

180 355		$18.00		Clutch Slave Cylinder HOSE

Rear Handbrake Assembly FELT WASHERS

Ideal washer = 1/16” Thick Felt with a ¾” Outside Diameter & 3/16” Inside Diameter

Exterior Door Handle Inside Button SPRINGS   #71451 S (Stainless Steel)	$4.70/each

From Century Spring CORP P O BOX 15287 Los Angeles CA 90015